Ladder logic blocks

Ladder Logic software supports following blocks

Contact blocks
	Normally open contact
	Normally closed contact, / “not” contact
Coils
	Normally de-energized coil
	Normally energized coil, / “not” coil
Timers
	On-delay timer
	Off-delay timer
	Pulse timer
Latch
	Latch

Ladder example 1 – motor control latch circuit

Description: There are two keys for motor control – key for motor start (at input X0) and another one for stop (at input X1). Motor relay connected to output Y0. Momentary pressing of start key starts motor, momentary pressing of stop key stops motor.
Translated code is (in loop(){...})

…
/Rung 1
in(X0);
or(Y0);
andNot(X1);
out(Y0);
…

And solution using latch block
Translated code
…
//Rung 1
in(X0);
latch(Y0,X1);
…
Ladder example 2 – flashlight

Description: Control key pressing on X0 starts lamp on Y0 flashing with period of 1 second, and another pressing stops this.

Translated code is (in loop(){...})
…
unsigned int AUX0, AUX1; //aux variables
unsigned int CLR001, CLR003; //addition variables for lines
unsigned long TMR1=0, TMR2=0; //timer variables
…
//Rung 1
in(X0);
andNot(AUX1);
out(CLR001);
in(AUX0);
andNot(X0);
or(CLR001);
out(AUX0);

//Rung 2
inNot(X0);
and(AUX0);
out(CLR003);
in(AUX1);
and(X0);
out(AUX1);

//Rung 3
in(AUX0);
timerPulse(TMR1, 200, TMR2, 800);
out(Y0);